## Slide 1: AL-AYEN UNIVRSITY COLLEGE OF ENGINEERING
RESERVOIR ENGINEERING I
NASIR ATALLAH
ASMAA AHMED
2022-2023
Introduction

## Slide 2
Outline
Petroleum system (PS)
Elements & processes of PS
Reservoir rocks
Significance of rock properties
Methods of rock properties measurements
Summary
Introduction

## Slide 3
Petroleum system (PS)
The petroleum system (PS) is a core concept in Petroleum geology
PS encompasses all the key elements & processes in the formation of hydrocarbons.
Key elements
Source rock
Cap rock
Processes
Trap formation
Generation
Reservoir rock
Migration
Accumulation

## Slide 4
Elements & processes of PS
1- Source rock
2- Reservoir rock
3- Cap rock or seal
4- Trap
5- Migration

## Slide 5
Elements & processes of PS: Source rock
Sedimentary rock made of shale or limestone.
Contains the precursors of hydrocarbon formation & organic matters.
Organic matter subjected to high temperature for a long time to convert into hydrocarbon.
Hydrocarbon can be generated depending on temperature/depth limit
The limit is called the oil window or oil kitchen

## Slide 6
Elements & processes of PS: Cap rock
Low permeability rock
Restricts hydrocarbons to escape from the reservoir
Made of chalks, shale or evaporates

## Slide 7
Elements & processes of PS: Trap
The trap is structural or stratigraphic feature
Ensures a fixed and firm position of seal and reservoir which avoids the escape of hydrocarbons
Three types of traps: Structural, Stratigraphic and combination

## Slide 8
Dome-Shaped and Anticline:
Structural Hydrocarbon Traps
Fault Trap
Salt-Dome
Notes: The dome above shows gravity separation of fluids. Shale comprises the upper and lower confining beds.

## Slide 9
Oil/Gas
Oil/Gas
Stratigraphic Hydrocarbon Traps
Uncomformity
Unconformity
Pinch out
Notes: Stratigraphic hydrocarbon traps occur where reservoir facies pinch into impervious rock such as shale, or where they have been truncated by erosion and capped by impervious layers above an unconformity.

## Slide 10
Elements & processes of PS: Migration
Process of moving oil and gas from the source rock to the reservoir rock
The main factors of the oil and gas migration:
Compression
Buoyancy
Thermal expansion
Maturation (increase in volume with time)
Gravitational separation of hydrocarbons & water from each other

## Slide 11
Reservoir rocks
The reservoir is the portion of rock containing the pool of petroleum
Composed of sedimentary rocks, such as sandstones, limestones and dolomites
Must be a large enough capacity to store economically viable amounts of hydrocarbon
The hydrocarbon must flow at economical rates when penetrated by a well

## Slide 12
Reservoir rocks
Reservoir lithology
The term lithology is used as a gross identification for a rock layer in the subsurface and uses familiar names such as:
Sandstone, Limestone, Dolomite, Claystone (or clay)
Lithology identification is fundamental to all reservoir characterization.
Understanding reservoir lithology is the foundation from which all other petrophysical calculations are made.

## Slide 13
Reservoir rocks
Reservoir lithology: Clastic & Carbonates

## Slide 14
Reservoir rocks
Major reservoir rock properties:
1- Porosity, Φ
2- Permeability, K
3- Rock compressibility, Cf
4- Rock resistivity, Rt
5- Saturation, Sw, So, Sg
6- Wettability
7- Capillary pressure, Pc
8- Relative permeabilities, Kro, Krw, Krg

## Slide 15
Significance of rock properties
Rock properties in conjunction with fluid properties are very important for
Reservoir engineers

## Slide 16
Why are reservoir rock properties so important?
1-How much oil? Φ, Swc
2-How much oil can be recovered? Φ, Sor, Co, Cf, Cg, Cw
3-How fluids flow in the reservoir? K, Ke, Ko, Krw, Krg
4-To predict production profile Kro, Krw, Krg, Sw, So, Sg
5-Predict change in reservoir pressure Co, Cf, Cg, Cw
Significance of rock properties

## Slide 17
Coring is a process of taking samples (Cores) from a reservoir.
Cores can be taken during drilling operations as a continuous section or as sidewell plugs from the wellbore wall
Measurement of rock properties: Coring
Two ways can be used to determine rock properties:
1- Coring
2- Well logging
Coring

## Slide 18
Samples are cleaned & subjected to many laboratory measurements
Samples are then analysed to determine the reservoir properties.
Two distinct methods for core analysis: Routine core analysis and Special core analysis (SCAL)
Measurement of rock properties: Coring

## Slide 19
Measurement of rock properties: Coring
Routine & SCAL
SCAL
Routine
Porosity
Horizontal & vertical perm.
Grain density
Lithology
Relative permeability
Capillary pressure
Saturation exponent, n
Cementation exponent, m

## Slide 20
Measurement of rock properties: Coring
Two types of coring:
Conventional coring (Whole coring)
Sidewell coring

## Slide 21
Measurement of rock properties: Coring
Whole coring
Continues section of rocks extracted from a well during drilling operations
Coring assembly & bit are used
The core bit is a hollow cylinder with cutters on the outside

## Slide 22
Measurement of rock properties: Coring
Whole coring
The cylindrical core is retain in the core barrel
Core diameter is typically from 1.75 to 5.25 inches and about 1m long
These core barrels are then cut into small pieces called plugs

## Slide 23
Measurement of rock properties: Coring
Whole coring
depth | lithology | porosity | Horizontal perm. | Vertical perm
3320 | S.St | 0.2 | 1000 | 100
3321 | S.St | 0.18 | 950 | 80
3322 | S.St | 0.25 | 1500 | 150
3323 | shale | 0.01 | 0.02 | 0.02
3324 | shale | 0.02 | 0.02 | 0.02
3325 | S.St | 0.25 | 1450 | 160
3326 | S.St | 0.23 | 1320 | 120
3327 | S.St | 0.27 | 2000 | 200
3319.5
3328

## Slide 24
Measurement of rock properties: Coring
Sidewell coring
Plugs of rock cut from the wellbore wall
Acquired by wireline-conveyed tools

## Slide 25
Measurement of rock properties: Well logging
Logging are a special tools lowered into the well
To examine the formation rocks
Obtain measurements about rock properties
Several tools are run at the same time as a logging string

## Slide 26
Measurement of rock properties: Well logs
Data are displaced as a series of measurements covering a depth range in a display called well logs
Data of each tool or many tools togother are shown in distinct tracks
Track 1
Track 3
Track 4
Track2

## Slide 27
Measurement of rock properties: Well logs
Logging tools designed for formation evaluation are based on:
1- Electrical measurements
Resistivity, Induction
2- Nuclear & radioactive measurements
Neutron, Density & Gamma ray
3- Acoustic measurements
Sonic