## Slide 1
AL-AYEN UNIVRSITY COLLEGE OF PETROLEUM ENGINEERING
TECHNICAL ENGLISH
Lecture #8: Reservoir Rock Properties
2022-2023
NASIR ALSHMLH
ASMAA ALGHAZI

## Slide 2
Reservoir Rocks Properties
Hydrocarbon traps may be illustrated by considering a porous, permeable formation that has been folded into an anticlinal trap by diastrophism and is enclosed between impermeable rocks.
The closure of the trap is the distance between the crest and the spill point (lowest point of the trap that can contain hydrocarbons). In most cases, the hydrocarbon trap is not filled to the spill point. It may contain a gas cap if the oil contains light hydrocarbons and the pressure-temperature relationship of the zone permits the existence of a gas zone at the top of the reservoir.
If a gas cap exists, the gas-oil contact is the deepest level of producible gas. Likewise, the oil-water contact is the lowest level of producible oil. Transition zones between various zones grading from high oil saturation to hydrocarbon-free water. For example, the water zone immediately below the oil-water contact is the bottom water, whereas the edge water is laterally adjacent to the oil zone.
The genesis of petroleum occurs in compacted clay and shale beds, which are essentially impermeable to fluid flow. The processes by which hydrocarbons migrate from the source rock to a porous, permeable reservoir are called primary migration. After leaving the source rock, the hydrocarbons migrate upward through permeable beds until they reach a sealed hydrocarbon trap where accumulation occurs forming a hydrocarbon reservoir. This process has been called secondary migration.

## Slide 3
Reservoir Rocks Properties
Porosity is an availability of pore spaces between rock particles. Porosity is a ratio of open space to total volume of rock and is calculated in percentage
Sand grains and particles of carbonate materials that make up sandstone and limestone reservoirs usually never fit together perfectly due to the high degree of irregularity in shape. The void space created throughout the beds between grains, called pore space or interstices, is occupied by fluids (liquids / gases). The porosity of a reservoir rock is defined as that fraction of the bulk volume of the reservoir that is not occupied by the solid framework of the reservoir. Engineering classification of porosity: Absolute porosity is the ratio of the total void space in the sample to the bulk volume of that sample. Effective porosity is the ratio of the interconnected pore volume to the bulk volume. Geological classification of porosity: Primary porosity pore spaces in which oil and gas are found originated when the sand beds were laid down. Secondary porosity is the result of geological processes (diagenesis and catagenesis) after the deposition of sediment.
Permeability is easiness with which fluid can move through porous rock.
High permeability means numerous channels for oil and gas migration.
A reservoir rock must have the ability to allow petroleum fluids to flow through its interconnected pores. This rock property is termed permeability. The permeability of a rock depends on the effective porosity. Therefore, permeability is affected by the rock grain size, grain shape, grain size distribution (sorting), grain packing and the degree of consolidation and cementation. Permeability is affected by the type of clay present, especially where fresh water is present.
French engineer Henry Darcy developed a fluid flow equation that since has become one of the standard mathematical tools of the petroleum engineer. One Darcy is a relatively high permeability and the permeability of most reservoir rock is less than one Darcy. The common measure of rock permeability is in millidarcies (mD) or μm2 in SI units.

## Slide 4
Reservoir Rocks Properties
The term absolute permeability is used if the porous rock is 100 % saturated with a single fluid (phase), such as water, oil or gas. When two or more fluids are present in the rock, the permeability of the rock to the flowing fluid is called effective permeability.
Capillary pressure is the difference in pressure between two immiscible fluids across a curved interface at equilibrium. Curvature of the interface is the consequence of preferential wetting of the capillary walls by one of the phases.
Wettability is the term used to describe the relative adhesion of two fluids to a solid surface. In a porous medium containing two or more immiscible fluids, wettability is a measure of the preferential tendency of one of the fluids to wet (spread or adhere) the surface.
In water-wet brine-oil-rock system, water will occupy the smaller pores and wet the major portion of the surfaces in the larger pores. In area of high oil saturation, the oil rests on a film of water spread over the surface. If the rock surface is preferentially water-wet and the rock is saturated with oil, water will imbibe into the smaller pores, displacing oil from the core when the system is in contact with water.
If the rock surface is preferentially oil-wet, even though it may be saturated with water, the core will imbibe oil into the smaller pores, displacing water from the core when it is contacted with water. Thus, a core saturated with oil is water-wet if it will imbibe water and, conversely, a core saturated with water is oil-wet if it will imbibe oil.
Actually, the wettability of a system can range from strongly water-wet to strongly oil-water depending on the brine-oil interactions with the rock surface. If no preference is shown by the rock to either fluid, the system is said to exhibit neutral wettability or intermediate wettability, a condition that one might visualize as being equally wet by both fluids (50 % \ 50 % wettability).

## Slide 5
1. Say whether the following statements are T ( True) or F (False). If F (False), correct them according to the text.
Exercises
1. Hydrocarbon traps are considered to be ones enclosed between permeable rocks.
2. Hydrocarbon traps occurred as a result of diastrophism.
3. Porous, permeable formation isn’t surrounded by impermeable rocks.
4. Oil and gas are trapped at the bottom of the anticline.
5. The hydrocarbon trap is not filled to the spill point.
6. The existence of a distinct gas zone at the top of the reservoir is allowed.
7. The gas-oil contact is the deepest level of producible gas.
8. The gas-oil and water-oil contacts are generally tilted.

## Slide 6
2. Put a preposition into the following gaps.
Exercises
Petroleum occurs ________ compacted clay and shale beds.
Hydrocarbons migrate _____ the source rock ______a porous, permeable reservoir.
______leaving the source rock, the hydrocarbons migrate upward __________permeable beds.
The salinity ________compaction fluids moving in an upward direction gradually increases ______precipitation occurs ____ _________supersaturation.
Secondary migration ______petroleum ends _____ the accumulation _______ a structural or stratigraphic trap.
The hydrocarbons accumulate ______the highest point _____ the trap.
Petroleum may be transported _______ another sedimentary sequence as a result _________rapid erosion and clastic transport.

## Slide 7
3. Match the word phrases in the left column with the word phrases in the right.
Exercises
1. a fluid flow
2. the degree
3. the ratio
4. large and flat
5. reservoirs
6. the location
7. both permeability and porosity
A. grains uniformly arranged
B. of effective permeability
C. are called anisotropic
D. of sedimentary rocks
E. equation
F. of the cementing material within the pore space.
G. of consolidation and cementation

## Slide 8
4. Read the sentences and decide whether they are True (T) or False (F). If False (F), correct the statements.
Exercises
In water–wet brine-oil-rock system, water will occupy the larger pores and wet the major portion of the surfaces in the smaller pores.
Water will saturate the smaller pores, displacing oil from the core when the system is in contact with water.
The wettability of a system can range from strongly water-wet to strongly oil-water depending on the brine-oil interactions with the rock surface.
The residual oil saturation of fractional-wettability rocks is usually low.
The water film between the rock and the oil in the pore isn’t stabilized by a double layer of magmatic forces.
Compounds displace the remaining water and react directly with the oil surface when the electrostatic force balance is destroyed.

## Slide 9
H.W. Compose collocations from the following terms.
Exercises
1.hydrocarbon A. rock
2. reservoir B. migration
3. capillary C. trap
4. secondary D. reservoir
5. stratigraphic E. pressure
6. hydrocarbon F. accumulation
7. interstitial G. formation
8. hydrodynamic H. water
9. cohesive I. shales
10. impermeable G. molecules