## Slide 1
COLLAGE OF DENTISTRY
الفرع العلمي:طب الاسنان
المادةDental Radiology :
المحاضرة:Digital imaging
رقم المحاضرة13 :
اسم تدريسي المادة:م.م مسار عبد الخالق

## Slide 2
Digital radiography, a technique devoid of traditional film and processing solutions, has become prevalent in both medicine and dentistry. Initially pioneered by Francis Mouyen in the mid-1980s, intraoral sensors were introduced for dental use, followed by the development of extraoral sensors for panoramic and cephalometric imaging. Unlike conventional techniques, digital radiography describes its output as "images" rather than "radiographs" or "x-ray film," marking a significant shift in terminology and technology

## Slide 3
Main Components of Digital Imaging System

## Slide 5
Methods of Acquiring a Digital Image
Methods of Acquiring a Digital Image

## Slide 6
PSP
PLATE

## Slide 7
Direct digital imaging systems are divided into two types:
Real time or corded
Photostimulable phosphor storage plate or cordless

## Slide 10
PSP
PLATE

## Slide 11
Advantages of CCD/ COMS:
The image appears on the monitor instantaneously.
Infection control is easier and quicker.
Advantages of PSP:
Detectors are thin and flexible, more comfortable for the patient, and easier for operator to use.
Cheaper, especially when multiple operatories are involved.

## Slide 12
Indirect digital imaging
In this method we have a CCD camera and computer.
In this method, an existing x –ray film is (digitized) using a CCD camera. The CCD camera scans the image convert the image, and then displayed it on the computer monitor. The resultant image is similar to copy of the image versus the original image.

## Slide 13
Step by step procedure
1. sensor preparation: The placement of the intraoral sensor in the mouth of patient is similar to the technique used in conventional film placement, but the number and size of the sensor vary with different manufactures, each sensor is sealed and water proofed and for infection control, the sensor must be covered with a disposable barrier because it cannot be sterilized.
Sensor placement: The sensor is held by bite block attachment or devices. The paralleling technique is the preferred exposure method because of dimensional accuracy of images and the ease of standardizing such images. Paralleling technique film holders must be used to stabilize to sensor in the mouth. As with conventional intraoral film, the sensor is centered over the area of interest. As in conventional radiography, the x –ray is aimed to strike the sensor. An electronic charge is produced on the surface of the sensor, this electronic signal is converted into digital form. The digital sensor in turn transmits this information to a computer then the image is processed by a computer and stored by the software.

## Slide 14
Digital radiographic image representation and manipulatio
Representation as Numbers and Pixels | Radiographic images within a computer are represented as a sequence of numbers, forming a grid or matrix of pixels
Pixel Rendering | Each pixel is assigned a number based on X-ray attenuation, determining its shade of grey
Range of Numbers and Shades of Grey | Typically ranges from 0 to 256, with 0 representing black, 256 representing white, and other numbers representing shades
Information and Resolution | Number and size of pixels, along with shades of grey, determine image information, file size, and resolution
Image Manipulation and Processing | Pixels can be assigned different numbers, pixel coordinates can be changed, and shades of grey can be altered
Limitations of Image Enhancement | Image enhancement can improve aesthetics but may compromise clinical information; computer cannot add real information

## Slide 16
Advantages over conventional film-based radiography

## Slide 18
Digital Subtraction Radiography:
Technique: Digital Subtraction Radiography involves capturing two identical images with virtually identical geometry but exposed at different times.
Purpose: It is used to detect radiographic changes that occur over time by subtracting one image from another, leaving only the changes between the two intact.
Sensitivity: Digital subtraction radiography is highly sensitive, capable of detecting minute changes as small as 0.12-mm, whereas visual examination of standard radiographs may miss changes of 0.85-mm.
Applications: It is particularly useful in the diagnosis of periodontal and carious lesions, which may progress slowly. It also aids in evaluating small changes in the condylar position and assessing osseous remodeling around hydroxyl apatite implants.